## Slide 1
Bus Arbitration / Bus Contention
Multiprocessor used a common bus
Multiprocessor system
Closely coupled system
Loosely coupled system
Every processor has its own local bus to connect with memory and I/O devices and all the processors are connected via the system bus
HUB
Processor 1
Processor 1
Processor 1
Processor 1
Processor 1
Example : LAN
All processors are connected with hub through bus. Hub is the bus master who decide which processor will get control of system bus and when.

## Slide 2
There are universal methods of bus arbitration:
Daisy chaining method
Polling method
Independence request method

## Slide 3
Daisy chaining method
BUS Master
Module 0
Module 1
Module N
8259 priority resolver
Grant
Request
Busy
In daisy chaining method all modules are connected with Bus master (8259) who is responsible to provide the system bus access.
It is also called as priority resolver.
There are total three important signals.
Grant , Request, Busy
Request : If any module wants bus access then that particular module will send bus request to bus master using this signal.
Grant : If no one module is accessing bus, bus master will provide permission to requested module using grant signal.
Busy : Bus is free or not this is inform by this signal.

## Slide 4
Daisy chaining method
BUS Master
Module 0
Module 1
Module N
8259 priority resolver
Grant
Request
Busy
If nobody using BUS, then the status of BUSY signal is 0 which means bus is free
= 0
2. When request is 1, which means someone wants bus access.
Every processor is working on its own data
= 1
3. If Busy = 0, bus master grant the permission for first module, i.e. physically closest module.
4. If module don’t want the bus access it will simply pass the grant to next module
Grant
5. If module want’s the bus access it will make BUS = 1 and uses the bus.
Advantages :
Simplest for small network.
Disdvantages :
Poor performance : It is slow because one by one grant is passes through modules.
What if network is bigger????
2. Poor reliability : If any one module fails grant will be lost.
3. Poor priority mechanism : get the grant for module which is physically closer the bus arbiter
Example :
If Module 1 and Module 7 request for bus access simultaneously then Module 1 will get first access.

## Slide 5
2. Polling chaining method
BUS Master
Module 0
Module 1
Module N
8259 priority resolver
Request
Busy
Bus master don’t have an idea about the requested module.
Bus master will ask every module , about the request by polling
N no. of modules and only one request line
Grant/ Poll
If there is a bus request i.e. Request = 1, priority resolver not circulate the grant signal. Instead of that it will poll (ask) to every module using poll lines.
Poll Numbers = Address of every module
Example :
If 8 modules then,
23 = 8 addresses
M0 | 000
M1 | 001
…. | ….
M7 | 111
2. If poll matches, then corresponding module will set the BUSY signal. i.e. BUSY = 1
Example :
If module 1 wants the bus access then module 1 will send request
Bus master don’t know the address of requested module. So it will start with polling
First it will send 000 to all
0
0
0
000
000
000
Address matched with module 0 but he was not the requester & for M1 address not matched
Now it will send 001 to all
0
0
1
001
001
001
Address matched because this module is requester.
Busy = 1
Advantages :
1. Priority is best
2. Reliability is best
If any module fails doesn't matter
Disadvantage :
Physical no change.
No more module can add due to polling.

## Slide 6
3. Independence Request method
BUS Master
Module 0
Module 1
Module N
8259 priority resolver
Grant 0
Request 0
Busy
In independence request method there separate grant and request signal for all the modules and only one Busy signal
Grant 1
Request 1
Grant N
Request N
If any module wants bus access it will send bus request and if busy = 0 then it will receive grant signal from bus master.
After receiving grant, corresponding module set the Busy signal i.e. Busy = 1
Advantages :
Super in priority and reliability
Faster
Disadvantages:
No simple if modules increases.