## Slide 1: Memory Bank of 8086

## Slide 2
Memory
00000
00001
00002
00003
00004
00005
.
FFFFF
Individual memory location size is 8 bits
Byte
8086 Processor
8086 is 16 bit processor hence can access 16 bits at a time.
1st cycle
2nd cycle
Hence processor will require 2 cycles to fetch 16 bits from memory.
Why memory bank required??????
To avoid above problem memory bank concept is used. Processor can access two consecutive memory locations in one cycle.

## Slide 3: Memory bank:
Even Address Memory Bank
Odd Address Memory Bank
Even Memory
.
.
00008
00006
00004
00000
Byte
Odd Memory
Byte
FFFFE
00002
.
.
00009
00007
00005
00001
FFFFF
00003
8086 Processor
Processor can read or write two memory locations of 16 bit in single cycle.

## Slide 5
Block diagram of 8086 memory bank
BHE | A0 | Bank
0 | 0 | Both bank (16 bit)
0 | 1 | Odd (8 bit)
1 | 0 | even (8 bit)
1 | 1 | No Bank

## Slide 6
Chip 1
CS
CS
To start the working of Chip, every chip has to activate.
To activate or enable particular chip there is a pin which is called as chip select .
This pin is active low, hence CS=0 will enable the chip.
0
Chip 1
1
For 8086 memory chip :
Chip 1
CS
CS
0
Chip 1
0
BHE
A0

## Slide 8
Different Types of memory access :
Accessing Even Addressed Byte
Accessing Odd Addressed Byte
Accessing Even Addressed word
Accessing Odd Addressed Word
Lower byte i.e. Lower 8 bits
Higher byte i.e. Higher 8 bits
All 16 bits , first lower then higher
All 16 bits , first higher then Lower

## Slide 9
1. Accessing Even Addressed Byte
Lower byte i.e. Lower 8 bits
Processor wants to access 8 bits of even memory locations.
0
Activates the chip
1
Diasabled the chip
How many cycles are required to perform this operation ??????
1 Cycle
ODD
Higher
EVEN
Lower

## Slide 10
2. Accessing Odd Addressed Byte
Higher byte i.e. Higher 8 bits
ODD
Higher
EVEN
Lower
Processor wants to access 8 bits of odd memory locations.
0
Activates the chip
1
Disabled the chip
How many cycles are required to perform this operation ??????
1 Cycle

## Slide 11
3. Accessing Even Addressed Word
All 16 bits , first lower 8 bits then higher 8 bits
ODD
Higher
EVEN
Lower
Processor wants to access 16 bits of even memory locations.
1
2
0
0
How many cycles are required to perform this operation ??????
1 Cycle

## Slide 12
4. Accessing Odd Addressed Word
All 16 bits , first Higher 8 bits then Lower 8 bits
1
2
How many cycles are required to perform this operation ??????
2 Cycle